## Slide 1: C h a p t e r 4
Introduction to the Thumb Instruction Set

## Slide 2: Thumb Register Usage
Thumb encodes a subset of the 32-bit ARM instructions into a 16-bit instruction set space.
Thumb has higher code density .
a Thumb implementation of the same code takes up around 30% less memory than the equivalent ARM implementation.
In Thumb state, you do not have direct access to all registers.
Only the low registers r0 to r7 are fully accessible,
The higher registers r8 to r12 are only accessible with MOV, ADD, or CMP instructions.
CMP and all the data processing instructions that operate on low registers update the condition ﬂags in the cpsr.
To alter the cpsr or spsr, you must switch into ARM state to use MSR and MRS
You need to be in ARM state to access the coprocessor for conﬁguring cache and memory management.

## Slide 3: ARM-Thumb Interworking
ARM-Thumb interworking is the name given to the method of linking ARM and Thumb code together for both assembly and C/C++.
To call a Thumb routine from an ARM routine, the core has to change state. This state change is shown in the T bit of the cpsr.
BX and BLX branch instructions cause a switch between ARM and Thumb state while branching to a routine.
The BLX instruction was introduced in ARMv5T.

## Slide 4: Other Branch Instructions
There are two variations of the standard branch instruction.
The ﬁrst is similar to the ARM version and is conditionally executed.
The second version removes the conditional part of the instruction and expands the effective branch.
Thumb instructions. The ﬁrst instruction in the pair holds the high part of the branch offset, and the second the low part.
These instructions must be used as a pair.

## Slide 5: Data Processing Instructions
The data processing instructions manipulate data within registers.
They include move instructions, arithmetic instructions, shifts, logical instructions, comparison instructions, and multiply instructions.
The Thumb data processing instructions are a subset of the ARM data processing instructions.
Most Thumb data processing instructions operate on low registers and update the cpsr.

## Slide 6: Single-Register Load-Store Instructions
The Thumb instruction set supports load and storing registers, or LDR and STR.
The offset by register uses a base register Rn plus the register offset Rm.
Load/store register [Rn, Rm]
The second uses the same base register Rn plus a 5-bit immediate or a value dependent on the data size.
Base register offset [Rn, #immediate]

## Slide 7: Stack Instructions
The Thumb stack operations are different from the equivalent ARM instructions because they use the more traditional POP and PUSH concept.
The interesting point to note is that there is no stack pointer in the instruction.
This is because the stack pointer is ﬁxed as register r13 in Thumb operations and sp is automatically updated.
The PUSH register list also can include the link register lr
similarly the POP register list can include the pc.

## Slide 8: Software Interrupt Instruction
Thumb software interrupt (SWI) instruction causes a software interrupt exception.
If any interrupt or exception ﬂag is raised in Thumb state, the processor automatically reverts back to ARM state to handle the exception.
The Thumb SWI instruction has the same effect and nearly the same syntax as the ARM equivalent.

## Slide 9: Summary
All Thumb instructions are 16 bits in length.
Thumb provides approximately 30% better code density over ARM code.
Most code written for Thumb is in a high-level language such as C and C .
ARM-Thumb interworking. Interworking uses the branch exchange (BX) instruction and branch exchange with link (BLX) instruction to change state and jump to a speciﬁc routine.
The Thumb instruction set includes POP and PUSH instructions as stack operations.
There are no Thumb instructions to access the coprocessors.