## Slide 1: c h a p t e r 6
Writing and Optimizing ARM Assembly Code

## Slide 2
For maximum performance, you can optimize critical routines using hand-written assembly.
Writing assembly by hand gives you direct control of three optimization tools that you cannot explicitly use by writing C source:
  Instruction scheduling
  Register allocation
  Conditional execution
It shows you how to replace a C function by an assembly function that you can then optimize for performance.

## Slide 3: Profiling and Cycle Counting
A proﬁler is a tool that measures the proportion of time or processing cycles spent in each subroutine.
You use a proﬁler to identify the most critical routines.
A cycle counter measures the number of cycles taken by a speciﬁc routine.
The ARM simulator used by the ADS1.1 debugger is called the ARMulator and pro- vides proﬁling and cycle counting features.
ARM implementations do not normally contain cycle-counting hardware
easily measure cycle counts you should use an ARM debugger with ARM simulator.

## Slide 4: Instruction Scheduling
The time taken to execute instructions depends on the implementation pipeline.
Instructions that are conditional on the value of the ARM condition codes in the cpsr take one cycle
ALU operations such as addition, subtraction, and logical operations take one cycle.
If you use a register-speciﬁed shift, then add one cycle.
Load and multiply instructions have delayed results in many implementations.
  Scheduling of load instructions
  Load Scheduling by Preloading
  Load Scheduling by Unrolling

## Slide 5: Register Allocation
You can use 14 of the 16 visible ARM registers to hold general-purpose data.
The other two registers are the stack pointer r13 and the program counter r15.
    Allocating Variables to Register Numbers
      it is best to start by using names for the variables, rather than explicit register numbers.
      Register names increase the clarity and readability of optimized code.
      Reduce the number of registers we require by performing fewer operations in each loop.

## Slide 6
    Using More than 14 Local Variables
      If you need more than 14 local 32-bit variables in a routine, then you must store some variables on the stack.
    Making the Most of Available Registers
      There are several tricks you can use to ﬁt several sub-32-bit length variables into a single 32-bit register
      thus can reduce code size and increase performance.
To ease register pressure you can sometimes store multiple values in the same register. For example, you can store a loop counter and a shift in one register. You can also store multiple pixels in one register.

## Slide 7: Conditional Execution
If you don’t specify a condition, the assembler defaults to the execute always condition (AL).
The other 14 conditions split into seven pairs of complements.
The conditions depend on the four condition code ﬂags N, Z, C, V stored in the cpsr register.
By default, ARM instructions do not update the N, Z, C, V ﬂags in the ARM cpsr.
For most instructions, to update these ﬂags you append an S sufﬁx to the instruction mnemonic.

## Slide 8: Looping Constructs
    Decremented Counted Loops
      If i is an array index, then you may want to count down from N 1 to 0 inclusive instead so that you can access array element zero.
    Unrolled Counted Loops
      Loop unrolling reduces the loop overhead by executing the loop body multiple times.
    ARM requires two instructions to implement a counted loop: a subtract that sets ﬂags and a conditional branch.
    Nested loops only require a single loop counter register, which can improve efﬁciency by freeing up registers for other uses.
    ARM can implement negative and logarithmic indexed loops efﬁciently.

## Slide 9: Bit Manipulation
To implement packing efﬁciently on the ARM we use a 32-bit register as a buffer to hold four bytes, in big-endian order.
The ARM can pack and unpack bits efﬁciently using logical operations and the barrel shifter.
To access bitstreams efﬁciently use a 32-bit register as a bitbuffer. Use a second register to keep track of the number of valid bits in the bitbuffer.
To decode bitstreams efﬁciently, use a lookup table to scan the next N bits of the bitstream. The lookup table can return codes of length at most N bits directly, or return an escape character for longer codes.

## Slide 10: Efﬁcient Switches
A switch or multiway branch selects between a number of different actions.
Make sure the switch value is in the range 0 x < N for some small N. To do this you may have to use a hashing function
  Use the switch value to index a table of function pointers or to branch to short sections of code at regular intervals. The second technique is position independent; the ﬁrst isn’t.
  Handling Unaligned Data
Recall that a load or store is unaligned if it uses an address that is not a multiple of the data transfer width.
The simplest method is to use byte loads and stores to access one byte at a time. This is the recommended method for any accesses that are not speed critical.
If performance is an issue, then use multiple routines, with a different routine optimized for each possible array alignment.