## Slide 1
ARM Instruction Set
By Khushal

## Slide 2
Introduction
Different ARM architecture support different instructions.
Code write fro architecture ARMv4T should execute on an ARMv5TE processor but not vice versa possible.

## Slide 3
Instructions Set

## Slide 4
Instructions Set

## Slide 5
Addition
As ARM based on RISC arch, all arithmatic operations done through registers.
Load and store pattern use
Instruction Syntax | Destination Register | Source Register 1 | Source Register 2
ADD r3, r1, r2 | r3 | r1 | r2

## Slide 6
Data Processing Instructions
Its manipulate data within registers.
There are move, arithmetic, logical, comparison and multiply instructions.
Instructions can process one of their operands using the barrel shifter.

## Slide 7
Move Instructions
It copies N into a destination register Rd, where N is a register or immediate value.
Syntax: <instruction>{<cond>}{S} Rd, N
MOV | Move a 32-bit value into a register | Rd = N
MVN | Move the NOT of the 32-bit value into a register | Rd = ~ N

## Slide 8
Barrel Shifter
ARM processor shift the 32-bit binary pattern in one of the source registers left or right by a specific number of positions before it enters the ALU.
This shift increases the power and flexibility of many data processing operations.

## Slide 9
Barrel Shifter

## Slide 10
Arithmetic Instructions
ADC | add two 32-bit values and carry | Rd = Rn + N + carry
ADD | add two 32-bit values | Rd = Rn + N
RSB | reverse subtract of two 32-bit values | Rd = N − Rn
RSC | reverse subtract with carry of two 32-bit values | Rd = N − Rn − !(carry flag)
SBC | subtract with carry of two 32-bit | values Rd = Rn − N − !(carry flag)
SUB | subtract two 32-bit values | Rd = Rn − N

## Slide 11
Logical Instructions
AND | logical bitwise AND of two 32-bit values | Rd = Rn & N
ORR | logical bitwise OR of two 32-bit values | Rd = Rn ¦ N
EOR | logical exclusive OR of two 32-bit values | Rd = Rn ∧ N
BIC | logical bit clear (AND NOT) | Rd = Rn & ∼N

## Slide 12
Comparison Instructions
CMN | compare negated | flags set as a result of Rn + N
CMP | compare | flags set as a result of Rn − N
TEQ | test for equality of two 32-bit values | flags set as a result of Rn ∧ N
TST | test bits of a 32-bit value | flags set as a result of Rn & N

## Slide 13
Branch Instructions
B | branch | pc = label
BL | branch with link | pc = label lr = address of the next instruction after the BL
BX | branch exchange | pc = Rm & 0xfffffffe, T = Rm & 1
BLX | branch exchange with link | pc = label, T = 1 pc = Rm & 0xfffffffe, T = Rm & 1 lr = address of the next instruction after the BLX
The address label is stored in the instruction as a signed pc-relative offset and
must be within approximately 32 MB of the branch instruction. T refers to the
Thumb bit in the cpsr.

## Slide 14
Load-Store Instructions
Load-store instructions transfer data between memory
and processor registers.There are three types of
load-store instructions:
1. single-register transfer,
2. multiple-register transfer,
3. swap.

## Slide 15
Single-register Transfer
LDR | load word into a register | Rd <- mem32[address]
STR | save byte or word from a register | Rd -> mem32[address]
LDRB | load byte into a register | Rd <- mem8[address]
STRB | save byte from a register | Rd -> mem8[address]

## Slide 16
Program Status Register Instructions
The ARM instruction set provides two instructions to directly control a program status register (psr).
The MRS instruction transfers the contents of either the cpsr or spsr into a register.
The MSR instruction transfers the contents of a register into the cpsr or spsr.

## Slide 17
Coprocessor Instructions
Coprocessor instructions are used to extend the instruction set.
A coprocessor can either provide additional computation capability or be used to control the memory subsystem including caches and memory management.

## Slide 18
Loading Constants
There is no ARM instruction to move a 32-bit constant into a register.
ARM instructions are 32 bits in size, they obviously cannot specify a general 32-bit constant.

## Slide 19
ARMv5E Extensions

## Slide 20
Thanks...