Major number and Minor number:
-The major number is to identify the corresponding driver. Many devices may use the same major number. So we need to assign the number to each device which is using the same major number. So this is the minor number.
We can allocate the major and minor numbers in two ways.
1. Statically allocating ->register_chrdev_region
2. Dynamically Allocating ->alloc_chrdev_region

Statically allocating:
The return value from register_chrdev_region will be 0 if the allocation was successfully performed. In case of error, a negative error code will be returned, and you will not have access to the requested region.
The dev_t type (defined in <linux/types.h>) is used to hold device numbers—both the major and minor parts. dev_t is a 32-bit quantity with 12 bits set aside for the major number and 20 for the minor number.
If you want to create the dev_t structure variable for your major and minor number, please use the below function.
MKDEV(int major, int minor);

If you want to get your major number and minor number from dev_t, use the below method.
MAJOR(dev_t dev);
MINOR(dev_t dev);

If you pass the dev_t structure to this MAJOR or MONOR function, it will return that major/minor number of your driver.

Unregister the minor number and major number:
void unregister_chrdev_region(dev_t first, unsigned int count);
Device file for character driver:
The device file allows transparent communication between user-space applications and hardware.
All device files are stored in /dev directory
The device files are generally created during system installation and include every possible device driver.
Device file:

We can create a device file in two ways.
1. Manually
2. Automatically

Manually:
We can create the device file manually by using mknod.
mknod -m <permissions> <name> <device type> <major> <minor>
<name> – your device file name that should have a full path (/dev/name)
<device type> – Put c or b
c – Character Device
b – Block Device
Example:
sudo mknod -m 666 /dev/etx_device c 246 0

### Advantages
- Anyone can create the device file using this method.
- You can create the device file even before loading the driver.
Automatically:
The automatic creation of device files can be handled with udev. Udev is the device manager for the Linux kernel that creates/removes device nodes in the /dev directory dynamically. Just follow the below steps.
1. Include the header file linux/device.h and linux/kdev_t.h
2. Create the struct Class
3. Create Device with the class which is created by the above step

1.creating the class:
This will create the struct class for our device driver. It will create a structure under/sys/class/.
struct class * class_create (struct module *owner, const char *name);

Note, you can destroy the device using device_destroy().
void class_destroy (struct class * class, dev_t devt);

2.creating the device
struct device *device_create (struct *class, struct device *parent, dev_t dev, const char *fmt, ...);
void device_destroy (struct class * class, dev_t devt);

File operation :
We have learned the major, minor number, and device file . So, as I said earlier, we need to open, read, write, and close the device file. If we want to open, read, write, and close we need to register some structures to the driver.
-An inode is a file data structure that stores information about any Linux file except its name and data contains are
-Mode:
This keeps information about two things, one is the permission information, the other is the type of inode, for example an inode can be of a file, directory or a block device etc.
Owner Info: Access details like owner of the file, group of the file etc.
Size:  This location store the size of the file in terms of bytes.
Time Stamps:  it stores the inode creation time, modification time, etc.
Now comes the important thing to understand about how a file is saved in a partition with the help of an inode.
Block Size: Whenever a partition is formatted with a file system.It normally gets formatted with a default block size.

-The struct cdev is the kernel’s internal structure that represents char devices. struct cdev is one of the elements of the inode structure.
This is cdev structure. Here we need to fill the two fields,
1. file_operation (This we will see after this cdev structure)
2. owner (This should be THIS_MODULE)

-struct cdev structure encapsulates the file_operations structure and some other important driver information(major/minor no). It is the way of registering character driver with kernel.
The cdev structure is accessed by the kernel through the following API's:
cdev_init() - used to initialize struct cdev with the defined file_operations
cdev_add() - used to add a character device to the system.
cdev_del() - used to remove a character device from the system
After a call to cdev_add(), your device is immediately alive. All functions you defined (through the file_operations structure) can be called.

-A file_operations structure is called fops. Each field in the structure must point to the function in the driver that implements a specific operation or have to left NULL for unsupported operations.

-fields of file operation:
-struct module *owner: it is a pointer to the module that “owns” the structure. This field is used to prevent the module from being unloaded while its operations are in use. Almost all the time, it is simply initialized to THIS_MODULE, a macro defined in <linux/module.h>.
-ssize_t (*read) (struct file *, char _ _user *, size_t, loff_t *); : This is used to retrieve data from the device
-ssize_t (*write) (struct file *, const char _ _user *, size_t, loff_t *);:It is used to sends the data to the device.
-int (*ioctl) (struct inode *, struct file *, unsigned int, unsigned long);: The ioctl system call offers a way to issue device-specific commands
-int (*open) (struct inode *, struct file *);:this is always the first operation performed on the device file, the driver is not required to declare a corresponding method.
-int (*release) (struct inode *, struct file *);:This operation is invoked when the file structure is being released. Like open, release can be NULL.
-pr_info:printk with kernel_info priority
-Instead of doing echo and cat command in the terminal you can also use open(), read(), write(), close() system calls from user-space applications.
#### -kmalloc()
We will see the memory allocation methods available in the kernel, in our next tutorials. But now we will use only the kmalloc in this tutorial.
kmalloc function is used to allocate the memory in kernel space. This is like a malloc() function in userspace. The function is fast (unless it blocks) and doesn’t clear the memory it obtains. The allocated region still holds its previous content. The allocated region is also contiguous in physical memory.

-GFP_USER – Allocate memory on behalf of the user. May sleep.
GFP_KERNEL – Allocate normal kernel ram. May sleep.