Device Driver
Topics :
Passing Arguments to Device Driver.
Major Number and Minor Number.
By: Harish Panicker

---
Passing Arguments to Device Driver
Module Parameters Macros
module_param(name,type,perm);
module_param_array(name,type,num,perm);
module_param_cb(name, ops, arg, perm);
There are several types of permissions:
S_IWUSR
S_IRUSR
S_IXUSR
S_IRGRP
S_IWGRP
S_IXGRP
In this S_I is a common header.
R = read ,W =write ,X= Execute.
USR =user ,GRP =Group
Using OR ‘|’ (or operation) we can set multiple permissions at a time.

---
- Parameters may be passed to the modules during module
  insertion
- The macro “module_param (name, type, perm)” is used to
  initialize the parameter at runtime.
- It takes 3 arguments which are the parameter name,
  parameter type and the permissions associated with the
  parameter
- This macro may be defined anywhere in the module

---
Major & Minor Numbers
- Devices are referred to by names in the filesystem.
- These names are called device files or simply nodes in the Filesystem.
- They find their existence in the /dev directory of the filesystem.
- They provide an interface to a device from the user space and is common to the kernel space to access the device too.

---
Major & Minor Numbers
- On issuing an ls -al on the /dev directory, the following is listed
  crw-rw---- 1 root uucp 33, 3 Mar 20 2005 cux3
  crw-rw---- 1 root uucp 33, 4 Mar 20 2005 cux4
  brw-r----- 1 root disk 12, 1 Mar 20 2005 dos_cd1
  brw-rw----1 root disk 14, 0 Mar 20 2005 dos_hda
  lrwxrwxrwx 1 root root 8 Oct 4 15:38 dmdsp0 -> /dev/dsp
- ‘c’ at the beginning of the file attributes specifies that the device is a character device.
- ‘b’ indicates that the device is a block device.
- ‘l’ indicates a link to a device file present at an other location.

---
Major & Minor Numbers
- Major Number
  - The major number identifies the driver associated with the device
  - Multiple drivers may share major numbers
  - For example, a major number may identify a driver for a hard disk
- Minor Number
  - Used by the kernel to determine exactly which device is being referred
  - The minor numbers could serve as an index into a list of devices for the related driver
  - For example, a minor number may be used to refer to one of the 4 hard disks present in the system
Both the major number and minor number together are called
Device Numbers

---
Device Numbers
- Within the kernel, the dev_t type is used to hold device numbers.
- dev_t is a 32 bit quantity with 12 bits set aside for the major number and 20
  bits set aside for the minor number
- To create a device number, use
  dev_t MKDEV(int major, int minor)
- To obtain the major and minor parts of a dev_t, macros come in handy
  int MAJOR(dev_t dev)
  int MINOR(dev_t dev)
- Headers
  #include <linux/kdev_t.h>
  #include <linux/types.h>

---
Allocating Device Numbers in the Kernel
We can allocate the major and minor numbers in two ways.
- Statically allocating
- Dynamically Allocating
- To Statically allocating a device number , we can use below function
  – int register_chrdev_region (dev_t first, unsigned int count, char
  *name);
- To dynamically allocate a device number by the kernel, use
  the function
  – int alloc_chrdev_region (dev_t *dev, unsigned int firstminor,
  unsigned int count, char *name);
  – Returns 0 on successful allocation, Negative number if not
  allocated

---
Allocating Device Numbers in the Kernel
- Device numbers are freed with
  void unregister_chrdev_region (dev_t first, unsigned int count)
- Registering the device number in the init_module
- Un-register the device number in the cleanup_module
- Header
  #include <linux/fs.h>

---
THANKS